- Out line

We have one product which is called analog modification kit. In this documents we would like to explain concerning this analog modification kit AXU00160.

- Contents

  - Parts list in this analog modification kit

- Teaching pendant key sheet(AKP11620-01)

- Welding I/F card(ZUEP5354X)

  - Other necessary things for modification

- Latest software for analog (Modification robot’s latest software for analog)

- Down load software(Version later than 1.20)

- External Memory Software(Version later than 4.00)

- RS232C cable

- How to modify from digital to analog

Note : When you make this modification, basically you will lose all program data.

- Save origin data, ASS, AES and LIB by External Memory software(Do not save by backup. Save one by one.)

- Make maintenance memory clear

(In memory clear mode, you can make maintenance memory clear. The procedure is as followings. After into the memory clear mode, push key “0”, “0” and “Enter”. Then you will see the maintenance clear.(The message will be all memory clear))

- Change robot software from digital to analog by using down load software.

- Turn off the robot’s power.

- Change teaching pendant key sheet to analog type, and add Welder I/F card on the sequencer card.

- Turn on the robot’s power.

- Make maintenance memory clear

(In memory clear mode, you can make maintenance memory clear. The procedure is as followings. After into the memory clear mode, holding to push key “.”, and push key “3”, “9” and “Enter”. Then you will see the maintenance clear.(The message will be all memory clear))

- Load origin data, ASS, AES and LIB by External Memory software

- Check all setting and input necessary data.

Note : In case of modification from analog to digital, please make modification by reverse procedure as above procedure.